## Slide 1: Progettazione di Sistemi Digitali
Docente: Salvatore Pontarelli

## Slide 2: Informazioni
Email docente: salvatore.pontarelli@uniroma1.it
Orario delle lezioni:
  martedi dalle 11:00 alle 13:00
  venerdì dalle 10:00 alle 13:00
Ricevimento:
  Contattare il docente via email
Materiale didattico:
  Libro di testo (da cui sono tratti i lucidi)
    Harris & Harris, Digital Design and Computer Architecture, ARM Ed., Morgan Kaufmann 2016.
Modalità d'esame: esame finale scritto e orale

## Slide 3: Finalità del corso
Il corso di Progettazione di Sistemi Digitali tratta argomenti preliminari alla descrizione dell'organizzazione di un calcolatore: rappresentazione dell'informazione, progettazione di reti combinatorie e sequenziali, registri e loro interconnessione. Tale corso fornisce quindi gli strumenti necessari alla comprensione del funzionamento e delle problematiche di progetto di un calcolatore, argomenti che verranno trattati nel corso di Architettura degli Elaboratori.

## Slide 4: Programma
Il corso copre i seguenti argomenti:
basi della logica binaria: porte logiche, sistemi di numerazione, rappresentazione dell’informazione
progettazione di sistemi combinatori: equazioni booleane, algebra booleana, mappe K, blocchi combinatori, timing
progettazione di sistemi sequenziali: Latch e Flip-Flop, progettazione di logica sincrona, macchine a stati finiti, tempistiche della logica sequenziale.
linguaggi descrittivi hardware (hdl): logica combinatoria, logica sequenziale, macchine a stati finiti, system verilog, VHDL
blocchi digitali costitutivi: circuiti aritmetici, blocchi sequenziali, matrici di memoria, matrici logiche.

## Slide 5: Binary number system

## Slide 6
Decimal numbers
Binary numbers
Number Systems

## Slide 7
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two

## Slide 8
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 9
Two methods:
  Method 1:
    Find the largest power of 2 that fits,
    subtract
    if not zero, repeat
  Method 2:
    divide by 2,
    put the remainder to the left of the binary representation
Decimal to Binary Conversion

## Slide 10
  5310
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012
Decimal to Binary Conversion

## Slide 11
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
or
75/2 = 37 R1
37/2 = 18 R1
18/2 = 9 R0
9/2 = 4 R1
4/2 = 2 R0
2/2 = 1 R0
1/2 = 0 R1
Decimal to Binary Conversion

## Slide 12
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 13
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 14
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 15
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 16
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 17
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 18
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 19
Decimal
Binary
Addition

## Slide 20
Add the following 4-digit hex numbers
Subtract the following 4-digit hex numbers
Hexadecimal Addition Examples
3A09
1B17
3D09
1B27

## Slide 21
Add the following 4-digit hex numbers
Subtract the following 4-digit hex numbers
Hexadecimal Addition Examples
5520
3A09
1B17
101
3D09
1B27

## Slide 22
Add the following 4-digit hex numbers
Subtract the following 4-digit hex numbers
Hexadecimal Addition Examples
5520
3A09
1B17
101
21E2
3D09
1B27
1

## Slide 23
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 24
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 25
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 26
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 27
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 28
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 29
msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers
+

## Slide 30
“Taking the Two’s complement” flips the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 31
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 32
Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 33
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 34
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 35
Per la prossima lezione:
Fare esercizi PSD1-esercizi
Studiare paragrafi 1.4 e 5.3 del libro
Fine lezione