## Slide 1
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops

## Slide 2
Enabled flip-flop with clock gating
Enabled Flip-Flops

## Slide 3
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops

## Slide 4
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 5
Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?

## Slide 6
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops

## Slide 7
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
Sequential Logic

## Slide 8
Sequential circuits: all circuits that aren’t combinational
A problematic circuit: (Ring oscillator)
No inputs and 1-3 outputs
Astable circuit, oscillates
Period depends on inverter delay
It has a cyclic path: output fed back to input
Sequential Logic

## Slide 9
Supponendo tcd = tpd= 1ns
Calcolare la frequenza del segnale CLK
Esercizio:
CLK

## Slide 10
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock signal
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design

## Slide 11
Consists of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
    Computes the outputs
Finite State Machine (FSM)

## Slide 12
Next state determined by current state and inputs
Two types of finite state machines differ in output logic:
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs
Finite State Machines (FSMs)

## Slide 13
Traffic light controller
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
FSM Example

## Slide 14
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB
FSM Black Box

## Slide 15
FSM State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 16
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 17
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 
FSM State Transition Table

## Slide 18
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
FSM State Transition Table

## Slide 19
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X |  | 
0 | 0 | 1 | X |  | 
0 | 1 | X | X |  | 
1 | 0 | X | 0 |  | 
1 | 0 | X | 1 |  | 
1 | 1 | X | X |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table

## Slide 20
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table
S'1 = S1 Å S0
S'0 = S1S0TA + S1S0TB

## Slide 21
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table

## Slide 22
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0

## Slide 23
FSM Schematic: State Register

## Slide 24
FSM Schematic: Next State Logic

## Slide 25
FSM Schematic: Output Logic

## Slide 26
FSM Timing Diagram

## Slide 27
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler
FSM State Encoding

## Slide 28
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 29
Use One-hot encoding to design the traffic
light controller between Academic Avenue and Bravado Blvd
Exercise

## Slide 30
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01. Design Moore and Mealy FSMs of the snail’s brain.
Moore vs. Mealy FSM

## Slide 31
Mealy FSM: arcs indicate input/output
State Transition Diagrams
Notes: Fine lezione 5

## Slide 32
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table

## Slide 33
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table
S1’ = S0A
S0’ = A

## Slide 34
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
X | X | X | X | X
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table
S1’ = S0A
S0’ = A
Ho semplificato le funzioni sfruttando i don’t care dello stato S1S0=11

## Slide 35
Current State |  | Output
S1 | S0 | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
Moore FSM Output Table

## Slide 36
Moore FSM Output Table
Y = S1
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1

## Slide 37
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
State | Encoding
S0 | 0
S1 | 1
Mealy FSM State Transition & Output Table

## Slide 38
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
State | Encoding
S0 | 0
S1 | 1
Mealy FSM State Transition & Output Table
S0’ = A
Y = S0 A

## Slide 39
Moore FSM Schematic

## Slide 40
Mealy FSM Schematic

## Slide 41
Moore & Mealy Timing Diagram