## Slide 1
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 2
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 3
module counter #(parameter N = 8)
(input logic clk,
input logic reset,
output logic [N–1:0] q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else q <= q + 1;
endmodule
COUNTER

## Slide 4
Implementation:
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Shift Registers
Symbol:

## Slide 5
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 6
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 7
Trasmissione seriale
SR1
N
clk
SR2
N
Din
Dout
Load
Gli shifter registers possono essere utilizzzati per realizzare un trasmettitore seriale
Gli N bit di dato Din sono inviati allo shifter register SR1
I segnali di clock e Sout sono inviati al ricevitore SR2
SR2 viene utilizzato per ricostruire il dato Dout
Sout

## Slide 8
module shiftreg #(parameter N = 8)
(input logic clk,
input logic reset, load,
input logic sin,
input logic [N–1:0] d,
output logic [N–1:0] q,
output logic sout);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (load) q <= d;
else q <= {q[N–2:0], sin};
assign sout = q[N–1];
endmodule
SHIFT REGISTER WITH PARALLEL LOAD

## Slide 9: Memorie

## Slide 10
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 11
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 12
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 13
A RAM array has the following ports:
Address port with 2NxM bits has:
N address bits (inputs)
M bidirectional data bits. Or M read_data output bits + M write_data input bits
A WE (Write Enable) signal
Memory Arrays

## Slide 14
Memory Array Bit Cells

## Slide 15
0
1
Z
Z
Memory Array Bit Cells

## Slide 16
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array

## Slide 17
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 18
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 19
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 20
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 21
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM

## Slide 22
DRAM

## Slide 23
SRAM

## Slide 24
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 25
module ram #(parameter N = 6, M = 32)
(input logic clk,
input logic we,
input logic [N–1:0] adr,
input logic [M–1:0] din,
output logic [M–1:0] dout);
logic [M–1:0] mem [2**N–1:0];
always_ff @(posedge clk)
if (we) mem [adr] <= din;
assign dout = mem[adr];
endmodule
RAM

## Slide 26
module rom(input logic [1:0] adr,
output logic [2:0] dout):
always_comb
case(adr)
2'b00: dout = 3'b011;
2'b01: dout = 3'b110;
2'b10: dout = 3'b100;
2'b11: dout = 3'b010;
endcase
endmodule
ROM

## Slide 27
Esercizi
Esercizio 1: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 218 × 8
Esercizio 2: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 216 × 32
Esercizio 3: Costruire una memoria di 1 MB e larghezza di parola di 8 bits a partire da blocchi di memoria di dimensioni 218 × 32

## Slide 28: Logic Using ROM

## Slide 29
ROM: Dot Notation

## Slide 30
ROM Storage

## Slide 31
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
ROM Logic

## Slide 32
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 33
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 34
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
Logic with Any Memory Array

## Slide 35
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 36
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 37
Called lookup tables (LUTs): look up output at each input combination (address)
Logic with Memory Arrays

## Slide 38
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory
Multi-ported Memories