## Slide 1
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line
Parallelism

## Slide 2
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput
Parallelism Definitions

## Slide 3
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Parallelism Example

## Slide 4
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour
Parallelism Example

## Slide 5
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.
Parallelism Example

## Slide 6
Latency = ?
Throughput = ?
Spatial Parallelism

## Slide 7
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour
Spatial Parallelism

## Slide 8
Latency = ?
Throughput = ?
Temporal Parallelism

## Slide 9
Latency = 5 + (10) +15 = 30 minutes = 1/2 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism

## Slide 10
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 11
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 12
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 13
Esercizio FSM

## Slide 14
Esercizio FSM

## Slide 15
Esercizio FSM

## Slide 16
Esercizio FSM

## Slide 17
1. Progettare una FSM con 2 input (up/down) ed un output a 8 bit (contatore).
Contatore incrementa di 1 ogni volta che premo UP e decrementa di 1 ogni volta che premo DOWN.
Scrivere un testbench che controlla il funzionamento della FSM
Verilog FSMs

## Slide 18
Progettare una FSM con 2 input (up/down) ed un output a 8 bit (contatore).
Contatore incrementa di 1 ogni volta che premo UP e decrementa di 1 ogni volta che premo DOWN.
Scrivere un testbench che controlla il funzionamento della FSM e simularlo sul simulatore Basys3
Verilog FSM (1/2)

## Slide 19
Progettare una FSM con 2 input (up/down) ed due output a 4 bit (decine ed unita).
I due output decine ed unità sono 2 cifre di un numero in codifica BCD. Il numero viene incrementato di 1 ogni volta che premo UP e decrementato di 1 ogni volta che premo DOWN.
Scrivere un testbench che controlla il funzionamento della FSM e simularlo sul simulatore Basys3
Verilog FSM (2/2)