## Slide 1
Accedere all’area personale studente di INFOSTUD.
Selezionare CORSI DI LAUREA  Opinioni studenti
Inserire il codice OPIS 0Q25Y5DH e compilare il questionario
Questionario OPIS

## Slide 2
Chapter 5 :: Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Building blocks used to build microprocessor
Introduction

## Slide 4
1-Bit Adders

## Slide 5
1-Bit Adders

## Slide 6
1-Bit Adders

## Slide 7
The Full adder can be composed starting from 2 Half-Adders
1-Bit Adders
Full Adders from Half Adder

## Slide 8
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
Symbol
Multibit Adders (CPAs)

## Slide 9
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder

## Slide 10
tripple = NtFA
where tFA is the delay of a 1-bit full adder
Ripple-Carry Adder Delay

## Slide 11
Compute Cout for k-bit blocks using generate and propagate signals
Carry-Lookahead Adder

## Slide 12
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
Carry-Lookahead Adder

## Slide 13
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
Carry-Lookahead Adder

## Slide 14
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
Carry-Lookahead Adder

## Slide 15
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
  Pi = Ai + Bi
Carry-Lookahead Adder

## Slide 16
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
  Pi = Ai + Bi
    Carry out: The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
Carry-Lookahead Adder

## Slide 17
Now use column Propagate and Generate signals to compute Block Propagate and Generate signals for k-bit blocks, i.e.:
  Compute if a k-bit group will propagate a carry in (to the block) to the carry out (of the block)
  Compute if a k-bit group will generate a carry out (of the block)
Block Propagate and Generate

## Slide 18
Example: Block propagate and generate signals for 4-bit blocks (P3:0 and G3:0):
  P3:0 = P3P2 P1P0
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
Generally,
  Pi:j = PiPi-1 Pi-2Pj
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj ))
  Ci = Gi:j + Pi:j Cj-1
Block Propagate and Generate Signals

## Slide 19
32-bit CLA with 4-bit Blocks

## Slide 20
32-bit CLA with 4-bit Blocks
Critical path is reduced to tAND_OR

## Slide 21
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block
Carry-Lookahead Addition

## Slide 22
32-bit CLA with 4-bit Blocks

## Slide 23
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
Carry-Lookahead Adder Delay

## Slide 24
Esercizio

## Slide 25
Esercizio

## Slide 26
Esercizio

## Slide 27
Esercizio

## Slide 28
Esercizio

## Slide 29
Esercizio

## Slide 30
Esercizio