## Slide 1
32-bit CLA with 4-bit Blocks

## Slide 2
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
Carry-Lookahead Adder Delay

## Slide 3
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci-1
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Prefix Adder
Prefix Adder

## Slide 4
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)
Prefix Adder
Prefix Adder

## Slide 5
Generate and propagate signals for a block spanning bits i:j
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part (i:k) propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry
Prefix Adder
Prefix Adder

## Slide 6
16-Bit Prefix Adder Schematic
Prefix Adder

## Slide 7
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi, Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
Prefix Adder Delay
Prefix Adder

## Slide 8
Compare delay of: 32-bit ripple-carry, CLA, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
Adder Delay Comparisons
Prefix Adder

## Slide 9
Compare delay of: 32-bit ripple-carry, CLA, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns
Adder Delay Comparisons
Prefix Adder

## Slide 10
Subtracter

## Slide 11
Subtracter
Cin =1

## Slide 12
Comparator: Equality

## Slide 13
Comparator: Equality

## Slide 14
Comparator: Less Than

## Slide 15
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =
Shifters

## Slide 16
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 17
Shifter Design

## Slide 18
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 19
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 20
4 x 4 Multiplier

## Slide 21
Esercizi
Esercizio 1: Convertire i seguenti numeri decimali in complemento a 2 utilizzando 8 bits. Dividere il risultato per 4 utilizzando lo shift a destra. Riconvertire i numeri in decimale.
108
-13
105
-128
-99
Esercizio 2: Convertire i seguenti numeri decimali in complemento a 2 utilizzando 8 bits. Moltiplicare il risultato per 4 utilizzando lo shift a sinistra. Riconvertire i numeri in decimale.
108
25
-33
-32

## Slide 22
Esercizio (1+2+1 punti)
Dati i numeri in rappresentazione IEEE 754 half-precision X = 0xC080 e Y = 0x4440,
rappresentarli in notazione decimale in virgola mobile,
eseguire l’operazione X+Y e
rappresentare il risultato sia in notazione decimale a virgola mobile e sia in esadecimale.

## Slide 23
Esercizio (1+2+1 punti)
Dati i numeri in rappresentazione IEEE 754 half-precision X = 0xC080  -2.25
Y = 0x4440  4.25
X+Y = 2  4000