## Slide 1: Lezione 2

## Slide 2
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 3
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 4
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 5
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 6
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 7
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 8
Two common notations:
Fixed-point: binary point fixed
Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 9
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 10
Represent 7.510 using 4 integer bits and 4 fraction bits.
Fixed-Point Number Example

## Slide 11
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000
Fixed-Point Number Example

## Slide 12
Separare la parte intera da quella frazionaria
Per la parte intera usare gli algoritmi noti
moltiplicare la parte frazionaria p= 2 p
  Se p<1 la cifra successiva è 0.
  Altrimenti la cifra successiva è 1 ed alla parte frazionaria p =p-1 .
Se p  0 torna a 3. Altrimenti finisci.
Algoritmo conversione tra basi di numeri con la virgola

## Slide 13
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  Two’s complement:
Signed Fixed-Point Numbers

## Slide 14
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 15
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers

## Slide 16
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions – final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 17
Convert decimal to binary (don’t reverse steps 1 & 2!):
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 18
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 19
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 20
Write -58.2510 in floating point (IEEE 754)
Floating-Point Example

## Slide 21
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Floating-Point Example

## Slide 22
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
denormals | X | 00000000 | m ≠ 0 (-1)s x 2-126 x 0.m.
Floating-Point: Special Cases

## Slide 23
Half precision
Number | Sign | Exponent | Fraction
0 | X | 00000 | 0000000000
∞ | 0 | 11111 | 0000000000
- ∞ | 1 | 11111 | 0000000000
NaN | X | 11111 | non-zero
denormals | X | 00000 | m ≠ 0 (-1)s x 2-14 x 0.m.

## Slide 24
Half precision:
  16-bit
  1 sign bit, 5 exponent bits, 10 fraction bits
  bias = 15
  The minimum strictly positive (subnormal) value is 2−24 ≈ 5.96 × 10−8.
  The minimum positive normal value is 2−14 ≈ 6.10 × 10−5.
  The maximum representable value is (2−2−10) × 215 = 65504.
Floating-Point Precision

## Slide 25
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
  The minimum strictly positive (subnormal) value is 2−149 ≈ 1.4 × 10−45
  The minimum positive normal value is 2−126 ≈ 1.1 × 10−38.
  The maximum representable value is (2−2−23) × 2127 = 3.4 × 10+38
Floating-Point Precision

## Slide 26
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
  The minimum is 2.2 × 10−308
  The maximum representable value is 1.79 × 10+308
Floating-Point Precision