## Slide 1
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Floating-Point: Rounding

## Slide 2
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 3
Add the following floating-point numbers:
0x3FC00000 (1.5 = 1.5*2^0)
0x40500000 (3.25 = 1.625*2^1)
Floating-Point Addition Example

## Slide 4
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 5
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 6
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating-Point Addition Example

## Slide 7
Somma degli esponenti
Prodotto delle mantisse
Normalizzazione del risultato (se necessario)
Moltiplicazione Floating-Point

## Slide 8
Introduction
Logic Gates
Boolean Equations
Boolean Algebra
From Logic to Gates
Multilevel Combinational Logic
X’s and Z’s, Oh My
Karnaugh Maps
Combinational Building Blocks
Timing
Chapter 2 :: Topics

## Slide 9: Logic gates

## Slide 10
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 11
Single-Input Logic Gates

## Slide 12
Two-Input Logic Gates

## Slide 13
More Two-Input Logic Gates

## Slide 14
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 15
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 16
Nodes
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
Circuit elements
  E1, E2, E3
  Each a circuit
Circuits

## Slide 17
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs
Types of Logic Circuits

## Slide 18
Every element is combinational
Every node is either an input or connects to exactly one output
The circuit contains no cyclic paths
Example:
Rules of Combinational Composition

## Slide 19: Figure 2.7 Example circuits
Check if they are combinational

## Slide 20
Functional specification of outputs in terms of inputs
Example: S = F(A, B, Cin)
Cout = F(A, B, Cin)
Boolean Equations

## Slide 21
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Minterm: product that includes all input variables
ABC, ABC, ABC
Maxterm: sum that includes all input variables
(A+B+C), (A+B+C), (A+B+C)
Some Definitions

## Slide 22
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm

## Slide 23
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)

## Slide 24
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)

## Slide 25: Sum-of-Products Form
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)

## Slide 26: Sum-of-Products Form
Y = F(A, B) = AB + AB = Σ(1, 3)
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form

## Slide 27
Per la prossima lezione:
Fare esercizi PSD3-esercizi
Studiare capitolo 2 fino a 2.4
Fine lezione