## Slide 1
All Boolean equations can be written in POS form
Each row has a maxterm
Product-of-Sums (POS) Form

## Slide 2
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Product-of-Sums (POS) Form

## Slide 3
Y = F(A, B) = (A + B)(A + B) = Π(0, 2)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 4
Boolean Equations Example
You are going to the cafeteria for lunch
  You won’t eat lunch (E)
  If it’s not open (O) or
  If they only serve corndogs (C)
Write a truth table for determining if you will eat lunch (E).

## Slide 5
You are going to the cafeteria for lunch
  You won’t eat lunch (E)
  If it’s not open (O) or
  If they only serve corndogs (C)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 6: SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 7
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
SOP – sum-of-products
POS – product-of-sums
SOP & POS Form

## Slide 8
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged
Boolean Algebra

## Slide 9
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 10
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR
Dual: Replace: • with +
0 with 1

## Slide 11
Boolean Axioms
Number | Axiom | Dual | Name
A1 | B = 0 if B ≠ 1 | B = 1 if B ≠ 0 | Binary Field
A2 | 0 = 1 | 1 = 0 | NOT
A3 | 0 • 0 = 0 | 1 + 1 = 1 | AND/OR
A4 | 1 • 1 = 1 | 0 + 0 = 0 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | 1 + 0 = 0 + 1 = 1 | AND/OR
Dual: Replace: • with +
0 with 1
Notes: fine lezione 2

## Slide 12
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements

## Slide 13
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements
Dual: Replace: • with +
0 with 1

## Slide 14
Boolean Theorems of One Variable
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 15
B 1 = B
B + 0 = B
T1: Teorema dell’identità

## Slide 16
B 1 = B
B + 0 = B
T1: Teorema dell’identità

## Slide 17
B 0 = 0
B + 1 = 1
T2: Teorema annullamento

## Slide 18
B 0 = 0
B + 1 = 1
T2: Teorema annullamento

## Slide 19
B B = B
B + B = B
T3: Teorema dell'idempotenza

## Slide 20
B B = B
B + B = B
T3: Teorema dell'idempotenza

## Slide 21
T4: Teorema dell'involuzione (o della doppia negazione)
B = B

## Slide 22
T4: Teorema dell'involuzione (o della doppia negazione)
B = B

## Slide 23
B B = 0
B + B = 1
T5: Teorema dei complementi

## Slide 24
B B = 0
B + B = 1
T5: Teorema dei complementi

## Slide 25
Recap: Basic Boolean Theorems
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identità
T2 | B • 0 = 0 | B + 1 = 1 | Annullamento
T3 | B • B = B | B + B = B | Idempotenza
T4 | B = B |  | Involuzione
T5 | B • B = 0 | B + B = 1 | Complemento
Dual: Replace: • with +
0 with 1

## Slide 26
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 27
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento
How do we prove these are true?

## Slide 28
How to Prove
Method 1: Perfect induction
Method 2: Use other theorems and axioms to simplify the equation
  Make one side of the equation look like the other

## Slide 29
Proof by Perfect Induction
Also called: proof by exhaustion
Check every possible input value
If two expressions produce the same value for every possible input combination, the expressions are equal

## Slide 30
Example: Proof by Perfect Induction
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
0 0
0 1
1 0
1 1
B C BC CB

## Slide 31
0 0
0 0
0 0
1 1
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
Example: Proof by Perfect Induction
0 0
0 1
1 0
1 1
B C BC CB

## Slide 32
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 33
T7: Proprietà associativa
Number | Theorem | Name
T7 | (B•C) • D = B • (C • D) | Proprietà associativa

## Slide 34
T8: Proprietà distributiva
Number | Theorem | Name
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva

## Slide 35
T9: Assorbimento
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 36
T9: Assorbimento
Prove true by:
Method 1: Perfect induction
Method 2: Using other theorems and axioms
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 37
T9: Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
Method 1: Perfect Induction
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 38
T9: Assorbimento
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 39
T9: Assorbimento
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 40
T9: Assorbimento
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
Method 2: Prove true using other axioms and theorems.

## Slide 41
T9: Assorbimento
Method 2: Prove true using other axioms and theorems.
B•(B+C) = B•B + B•C T8: P. distributiva
= B + B•C T3: Idempotenza
= B•(1 + C) T8: P. distributiva
= B•(1) T2: Annullamento
= B T1: Identità
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 42
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento (assorbimento del complemento)
T10: IIo teorema dell’assorbimento
Prove true using other axioms and theorems:

## Slide 43
T10: IIo teorema dell’assorbimento
Prove true using other axioms and theorems:
B•C + B•C = B•(C+C) T8: P. Distributiva
= B•(1) T5’: Complemento
  = B T1: Identità
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 44
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento
Boolean Theorems of Several Vars
(duality)

## Slide 45
Dual: Replace: • with +
0 with 1
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars

## Slide 46
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars
Warning: T8’ differs from traditional algebra:
OR (+) distributes over AND (•)

## Slide 47
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars
Axioms and theorems are useful for simplifying equations.

## Slide 48
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals

## Slide 49
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C

## Slide 50
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C
Also called minimizing the equation

## Slide 51
Simplification methods
P. distributiva (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Io T. assorbimento (T9’) A + AP = A
IIo T. assorbimento (T10) PA + PA = P

## Slide 52
Simplification methods
P. distributiva (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Io T. assorbimento (T9’) A + AP = A
IIo T. assorbimento (T10) PA + PA = P
Espansione P = PA + PA
A = A + AP
Duplicazione A = A + A
Esempio di “semplificazione” PA + A = P + A
    PA + A = P + A

## Slide 53
Example
PA + A = P + A
Method 1: PA + A = PA + (A + AP) T9’ Assorbimento
= PA + PA + A T6 P. commutativa
= P(A + A) + A T8 P. distributiva
= P(1) + A T5’ Complemento
= P + A T1 Identità

## Slide 54
PA + A = P + A
Method 2: PA + A = (A + A) (A + P) T8’ P. distributiva
= 1(A + P) T5’ Complemento
= A + P T1 Identità
Example

## Slide 55
Y = A(AB + ABC)
Example 2:
Simplifying Boolean Equations

## Slide 56
Y = A(AB + ABC)
= A(AB(1 + C)) T8: P. distributiva
= A(AB(1)) T2’: Annullamernto
= A(AB) T1: Identità
= (AA)B T7: P. associativa
= AB T3: Idempotenza
Example 2:
Simplifying Boolean Equations

## Slide 57
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Example 6:
Simplifying Boolean Equations

## Slide 58
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations

## Slide 59
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations
This is called
multiplying out
an expression to get
sum-of-products (SOP) form.

## Slide 60
An expression is in sum-of-products (SOP) form when all products contain literals only.
SOP form: Y = AB + BC’ + DE
NOT SOP form: Y = DF + E(A’+B)
SOP form: Z = A + BC + DE’F
Multiplying Out: SOP Form

## Slide 61
Y = (A + C + D + E)(A + B)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = (C+D+E), Z = B and rewrite equation
Y = (A+X)(A+Z) substitution (X=(C+D+E), Z=B)
= A + XZ T8’: Distributivity
= A + (C+D+E)B substitution
= A + BC + BD + BE T8: Distributivity
or
Y = AA+AB+AC+BC+AD+BD+AE+BE T8: Distributivity
= A+AB+AC+AD+AE+BC+BD+BE T3: Idempotency
= A + BC + BD + BE T9’: Covering
Example:
Multiplying Out: SOP Form

## Slide 62
SOP – sum-of-products
POS – product-of-sums
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
Review: SOP & POS Form

## Slide 63
An expression is in product-of-sums (POS) form when all sums contain literals only.
POS form: Y = (A+B)(C+D)(E’+F)
NOT POS form: Y = (D+E)(F’+GH)
POS form: Z = A(B+C)(D+E’)
Factoring: POS Form

## Slide 64
Y = (A + B’CDE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = B’C, Z = DE and rewrite equation
Y = (A+XZ) substitution (X=B’C, Z=DE)
= (A+B’C)(A+DE) T8’: Distributivity
= (A+B’)(A+C)(A+D)(A+E) T8’: Distributivity
Example 1:
Factoring: POS Form

## Slide 65
Y = AB + C’DE + F
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Y = (AB+C’DE) +F T7: Associativity
= (AB+C’)(AB+DE)+F T8’: Distributivity
= (A+C’)(B+C’)(AB+D)(AB+E)+F T8’: Distributivity
= (A+C’)(B+C’)(A+D)(B+D)(A+E)(B+E)+F T8’: Distributivity
= (A+C’+F)(B+C’+F)(A+D+F)(B+D+F)(A+E+F)(B+E+F) T8’: Distributivity
Example 2:
Factoring: POS Form

## Slide 66
DeMorgan’s Theorem
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 67
DeMorgan’s Theorem
The complement of the product
is the
sum of the complements
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 68
DeMorgan’s Theorem: Dual
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 69
DeMorgan’s Theorem: Dual
The complement of the product
is the
sum of the complements.
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 70
DeMorgan’s Theorem: Dual
The complement of the product
is the
sum of the complements.
Dual: The complement of the sum
is the
product of the complements.
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 71
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 72
Y = (A+BD)C
DeMorgan’s Theorem Example 1

## Slide 73
Y = (A+BD)C
= (A+BD) + C
= (A•(BD)) + C
= (A•(BD)) + C
= ABD + C
DeMorgan’s Theorem Example 1

## Slide 74
Y = (ACE+D) + B
DeMorgan’s Theorem Example 2

## Slide 75
Y = (ACE+D) + B
= (ACE+D) • B
= (ACE•D) • B
= ((AC+E)•D) • B
= ((AC+E)•D) • B
= (ACD + DE) • B
= ABCD + BDE
DeMorgan’s Theorem Example 2

## Slide 76
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 77
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output
Bubble Pushing

## Slide 78
Bubble Pushing
What is the Boolean expression for this circuit?

## Slide 79
What is the Boolean expression for this circuit?
Y = AB + CD
Bubble Pushing

## Slide 80
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel
Bubble Pushing Rules

## Slide 81
Bubble Pushing Example

## Slide 82
Bubble Pushing Example

## Slide 83
Bubble Pushing Example

## Slide 84
Bubble Pushing Example

## Slide 85: BUBBLE PUSHING FOR CMOS LOGIC

## Slide 86: BUBBLE PUSHING FOR CMOS LOGIC

## Slide 87: BUBBLE PUSHING FOR CMOS LOGIC

## Slide 88: Completeness
NAND (and NOR) is functionally complete (universal)
NOT
AND
OR

## Slide 89: Esercizi De Morgan
Y= A’BC+(BC’)’+BC
= A’BC+(B’+C)+BC
= A’BC+B’+C+BC
= B’+C

## Slide 90: Esercizi De Morgan
Y= (A+B+C)’D+AD+B
= A’B’C’D+AD+B
= A’B’C’D+AD+B + A’BC’D
= A’B’C’D+AD+B + A’BC’D
= A’C’D+AD+B = A’C’D+AC’D+AD+B
= C’D+AD+B

## Slide 91: Esercizi De Morgan
Y = ABCD+A’BC’D+(B’+D)’E
= ABCD+A’BC’D+BD’E