## Slide 1: Progettazione di Sistemi Digitali (esercitazioni)
Docente: Salvatore Pontarelli

## Slide 2
Convert the following unsigned binary numbers to decimal. Show your work.
(a) 11102
(b) 1001002
(c) 110101112
(d) 0111010101001002
Exercise 1.14

## Slide 3
Repeat Exercise 1.14, but convert to exadecimal
Exercise 1.16

## Slide 4
Convert the following hexadecimal numbers to decimal. Show your work.
(a) 4E16
(b) 7C16
(c) ED3A16
(d) 403FB00116
Exercise 1.18

## Slide 5
Convertire i seguenti numeri in decimale
(a) 11104
(b) 4015
(c) 93212
(d) 3478
Convertire i seguenti numeri in base 2
(a) 31124
(b) 4018
(c) 7328
(d) 3478
Esercizio

## Slide 6
Convert the following two’s complement binary numbers to decimal
(a) 11102
(b) 1000112
(c) 010011102
(d) 101101012
Exercise 1.22

## Slide 7
Exercise 1.11 What is the smallest (most negative) 16-bit binary number that can be represented with:
(a) unsigned numbers?
(b) two’s complement numbers?
(c) sign/magnitude numbers?
Exercise 1.12 What is the smallest (most negative) 32-bit binary number that can be represented with:
(a) unsigned numbers?
(b) two’s complement numbers?
(c) sign/magnitude numbers?

## Slide 8
Exercise 1.43 How many bytes are in a 32-bit word? How many nibbles are in the word?
Exercise 1.44 How many bytes are in a 64-bit word?
Exercise 1.45 A particular DSL modem operates at 768 kbits/sec. How many bytes can it receive in 1 minute?
Exercise 1.46 USB 3.0 can send data at 5 Gbits/sec. How many bytes can it send in 1 minute?

## Slide 9
Exercise 1.29 Convert the following decimal numbers to 8-bit sign-magnitude number
  (a) 4210
  (b) −6310
  (c) 12410
  (d) −12810
  (e) 13310

## Slide 10
Exercise 1.21 Convert the following two’s complement binary numbers to decimal
  (a) 10102
  (b) 1101102
  (c) 011100002
  (d) 100111112
Exercise 1.23 Repeat Exercise 1.21, assuming the binary numbers are in sign/magnitude form rather than two’s complement representation.