## Slide 1
Chapter 3 :: Topics
Introduction
Latches and Flip-Flops
Synchronous Logic Design
Finite State Machines
Timing of Sequential Logic
Parallelism

## Slide 2
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about a circuit necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops
Introduction

## Slide 3
Sequential logic might explicitly remember certain previous inputs, or it might distill the prior inputs into a smaller amount of information called the state of the system
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 4
The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 5
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit

## Slide 6
Consider the two possible cases:
  Q = 0:
  then Q = 0, Q = 1 (consistent)
  Q = 1:
  then Q = 1, Q = 0 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis

## Slide 7
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch

## Slide 8
  S = 1, R = 0:
  then Q = 1 and Q = 0
  S = 0, R = 1:
  then Q = 0 and Q = 1
SR Latch Analysis
1

## Slide 9
  S = 1, R = 0:
  then Q = 1 and Q = 0
  Set the output
  S = 0, R = 1:
  then Q = 0 and Q = 1
  Reset the output
SR Latch Analysis
1
1

## Slide 10
  S = 0, R = 0:
  then Q = Qprev
  S = 1, R = 1:
  then Q = 0, Q = 0
SR Latch Analysis
1

## Slide 11
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis
1

## Slide 12
SR Latch Truth Table
The truth table in Figure summarizes these four cases.
The outputs, Q and Q, are normally complementary.
When neither input is asserted, Q remembers its old value, Qprev
Asserting both S and R simultaneously doesn’t make much sense

## Slide 13
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  (S = 1, R = 0, Q = 1)
  Reset: Make the output 0
  (S = 0, R = 1, Q = 0)
Must do something to avoid
invalid state (when S = R = 1)
SR Latch Symbol

## Slide 14
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch

## Slide 15
D Latch Internal Circuit (Do it)

## Slide 16
D Latch Internal Circuit (Done)

## Slide 17
Forme d’onda del latch
1: il latch è in hold. Non sappiamo il valore di Q: è ignoto o indeterminate (ho appena acceso l’alimentazione)
Notes: Fine lezione 4

## Slide 18
Forme d’onda del latch
1: il latch è in hold. Non sappiamo il valore di Q: è ignoto o indeterminate (ho appena acceso l’alimentazione)
2: il latch diventa trasparente. Ora Q=D.
Notes: Fine lezione 4

## Slide 19
Forme d’onda del latch
1: il latch è in hold. Non sappiamo il valore di Q: è ignoto o indeterminate (ho appena acceso l’alimentazione)
2: il latch diventa trasparente. Ora Q=D.
3: il D varia da 01. Q segue il valore di D (CLK=1)
Notes: Fine lezione 4

## Slide 20
Forme d’onda del latch
1: il latch è in hold. Non sappiamo il valore di Q: è ignoto o indeterminate (ho appena acceso l’alimentazione)
2: il latch diventa trasparente. Ora Q=D.
3: il D varia da 01. Q segue il valore di D (CLK=1)
4: il D varia da 10. Q segue il valore di D (CLK=1)
5: il D varia da 01. Q segue il valore di D (CLK=1)
Notes: Fine lezione 4

## Slide 21
Forme d’onda del latch
1: il latch è in hold. Non sappiamo il valore di Q: è ignoto o indeterminate (ho appena acceso l’alimentazione)
2: il latch diventa trasparente. Ora Q=D.
3: il D varia da 01. Q segue il valore di D (CLK=1)
4: il D varia da 10. Q segue il valore di D (CLK=1)
5: il D varia da 01. Q segue il valore di D (CLK=1)
HOLD: D varia da 10. Q NON segue il valore di D (CLK=0)
HOLD: D varia da 01. Q NON segue il valore di D (CLK=0)
Notes: Fine lezione 4

## Slide 22
Forme d’onda del latch
L’istante in cui CLK varia da 1 a 0 è l'ultimo istante in cui il latch campiona il valore di D.
Nella finestra in cui CLK rimane a 0, l'uscita del latch rimane al valore Qprev che aveva al momento in cui CLK si è abbassato
Notes: Fine lezione 4

## Slide 23
Disegnare un D-latch partendo da un MUX a 2 ingressi
Esercizio

## Slide 24
Disegnare un D-latch partendo da un MUX a 2 ingressi
Esercizio
CLK
Q
D

## Slide 25
Disegnare un latch SR partendo da un MUX a 2 ingressi
Esercizio

## Slide 26
Disegnare un latch SR partendo da un MUX a 2 ingressi
Esercizio
R
S
S
Q
1
0
X

## Slide 27
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
Activated on the clock edge
D Flip-Flop
Notes: Fine lezione 4

## Slide 28
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit

## Slide 29
D Latch vs. D Flip-Flop (Do it)

## Slide 30
D Latch vs. D Flip-Flop (Done)

## Slide 31
Registers: Multi-bit Flip-Flop