## Slide 1
Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge
If not, metastability can occur
Timing

## Slide 2
Setup time: tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time: thold = time after clock edge data must be stable
Aperture time: ta = time around clock edge data must be stable (ta = tsetup + thold)
Input Timing Constraints

## Slide 3
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
Output Timing Constraints

## Slide 4
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge
Specifically, inputs must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge
Dynamic Discipline

## Slide 5
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
Dynamic Discipline

## Slide 6
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥
Setup Time Constraint

## Slide 7
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
Setup Time Constraint

## Slide 8
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
Setup Time Constraint
(tpcq + tsetup): sequencing overhead

## Slide 9
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold <
Hold Time Constraint

## Slide 10
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
Hold Time Constraint

## Slide 11
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
tcd > thold - tccq
Hold Time Constraint

## Slide 12
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
Setup time constraint:
Hold time constraint:
Timing Analysis

## Slide 13
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Analysis

## Slide 14
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ ?
Hold time constraint:
tccq + tcd > thold ?
Timing Analysis
Add buffers to the short paths:

## Slide 15
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Timing Analysis
Add buffers to the short paths:

## Slide 16
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew

## Slide 17
In the worst case, CLK2 is earlier than CLK1
Tc ≥ ?
Setup Time Constraint with Skew

## Slide 18
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
Setup Time Constraint with Skew

## Slide 19
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Setup Time Constraint with Skew

## Slide 20
In the worst case, CLK2 is later than CLK1
Hold Time Constraint with Skew

## Slide 21
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
Hold Time Constraint with Skew

## Slide 22
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq
Hold Time Constraint with Skew