## Slide 1
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew

## Slide 2
In the worst case, CLK2 is earlier than CLK1
Tc ≥ ?
Setup Time Constraint with Skew

## Slide 3
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
Setup Time Constraint with Skew

## Slide 4
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Setup Time Constraint with Skew

## Slide 5
In the worst case, CLK2 is later than CLK1
Hold Time Constraint with Skew

## Slide 6
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
Hold Time Constraint with Skew

## Slide 7
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq
Hold Time Constraint with Skew

## Slide 8
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line
Parallelism

## Slide 9
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput
Parallelism Definitions

## Slide 10
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Parallelism Example

## Slide 11
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour
Parallelism Example

## Slide 12
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.
Parallelism Example

## Slide 13
Latency = ?
Throughput = ?
Spatial Parallelism

## Slide 14
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour
Spatial Parallelism

## Slide 15
Latency = ?
Throughput = ?
Temporal Parallelism

## Slide 16
Latency = 5 + (10) +15 = 30 minutes = 1/2 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism

## Slide 17
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 18
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 19
Temporal Parallelism
Compute max frequency, knowing that tpcq=15ps tgate_pd=40ps and tsu=65ps
Compute Latency
Compute Throughput

## Slide 20
Esercizio FSM

## Slide 21
Esercizio FSM

## Slide 22
Esercizio FSM

## Slide 23
Esercizio FSM