## Slide 1: Arithmetic circuits

## Slide 2
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =
Shifters

## Slide 3
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 4
Shifter Design

## Slide 5
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 6
Esercizi
Esercizio 1: Convertire i seguenti numeri decimali in complemento a 2 utilizzando 8 bits. Dividere il risultato per 4 utilizzando lo shift a destra. Riconvertire i numeri in decimale.
108
-13
105
-128
-99
Esercizio 2: Convertire i seguenti numeri decimali in complemento a 2 utilizzando 8 bits. Moltiplicare il risultato per 4 utilizzando lo shift a sinistra. Riconvertire i numeri in decimale.
108
25
-33
-32
Exercise 5.18 Design 4-bit left and right rotators. Sketch a schematic of your design.

## Slide 7
Exercises
Exercise 5.18 Design 4-bit left and right rotators. Sketch a schematic of your design.

## Slide 8
Exercises
Exercise 5.18 Design 4-bit left and right rotators. Sketch a schematic of your design.

## Slide 9
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 10
4 x 4 Multiplier

## Slide 11
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 12
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 13
Implementation:
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Shift Registers
Symbol:

## Slide 14
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 15
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 16
Trasmissione seriale
SR1
N
clk
SR2
N
Din
Dout
Load
Gli shifter registers possono essere utilizzzati per realizzare un trasmettitore seriale
Gli N bit di dato Din sono inviati allo shifter register SR1
I segnali di clock e Sout sono inviati al ricevitore SR2
SR2 viene utilizzato per ricostruire il dato Dout
Sout

## Slide 17: Memorie

## Slide 18
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 19
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 20
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 21
A RAM array has the following ports:
Address port with 2NxM bits has:
N address bits (inputs)
M bidirectional data bits. Or M read_data output bits + M write_data input bits
A WE (Write Enable) signal
Memory Arrays

## Slide 22
Memory Array Bit Cells

## Slide 23
0
1
Z
Z
Memory Array Bit Cells

## Slide 24
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array

## Slide 25
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 26
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 27
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 28
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 29
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM

## Slide 30
DRAM

## Slide 31
SRAM

## Slide 32
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 33
Esercizi
Esercizio 1: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 218 × 8
Esercizio 2: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 216 × 32
Esercizio 3: Costruire una memoria di 1 MB e larghezza di parola di 8 bits a partire da blocchi di memoria di dimensioni 218 × 32