## Slide 1: Memorie

## Slide 2
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 3
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 4
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 5
A RAM array has the following ports:
Address port with 2NxM bits has:
N address bits (inputs)
M bidirectional data bits. Or M read_data output bits + M write_data input bits
A WE (Write Enable) signal
Memory Arrays

## Slide 6
Memory Array Bit Cells

## Slide 7
0
1
Z
Z
Memory Array Bit Cells

## Slide 8
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array

## Slide 9
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 10
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 11
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 12
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 13
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM

## Slide 14
DRAM

## Slide 15
SRAM

## Slide 16
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 17
Esercizi
Esercizio 1: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 218 × 8
Esercizio 2: Costruire una memoria di 1 MB e larghezza di parola di 32 bits a partire da blocchi di memoria di dimensioni 216 × 32
Esercizio 3: Costruire una memoria di 1 MB e larghezza di parola di 8 bits a partire da blocchi di memoria di dimensioni 218 × 32

## Slide 18: Logic Using ROM/PLA/FPGA

## Slide 19
ROM: Dot Notation

## Slide 20
ROM Storage

## Slide 21
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
ROM Logic

## Slide 22
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 23
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 24
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
Logic with Any Memory Array

## Slide 25
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 26
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 27
Called lookup tables (LUTs): look up output at each input combination (address)
Logic with Memory Arrays

## Slide 28
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory
Multi-ported Memories

## Slide 29
PLAs (Programmable logic arrays)
  AND array followed by OR array
  Combinational logic only
  Fixed internal connections
FPGAs (Field programmable gate arrays)
  Array of Logic Elements (LEs)
  Combinational and sequential logic
  Programmable internal connections
Logic Arrays

## Slide 30
X = ABC + ABC
Y = AB
PLAs

## Slide 31
Un PLA (Programmable Logic Array) è una rete combinatoria con:
- M ingressi
- P uscite
3 stadi interni:
  uno stadio di inversione dei segnali di ingresso,
  una matrice di AND
  una matrice di OR.
PLAs

## Slide 32
Un PLA (Programmable Logic Array) è una rete combinatoria con:
Il piano AND può realizzare fino ad N implicanti
Questi implicanti possono essere utilizzati per realizzare fino a P funzioni logiche nella forma SOP
PLAs

## Slide 33
X = ABC + ABC
Y = AB
Esempio di programmazione PLA

## Slide 34
PLAs: Dot Notation

## Slide 35
Composed of:
  LEs (Logic elements): perform logic
  I/O Blocks (Input/output elements): interface with outside world
  Programmable interconnection: connect LEs and IOEs
  Some FPGAs include other building blocks such as multipliers and RAMs
FPGA: Field Programmable Gate Array

## Slide 36
General FPGA Layout

## Slide 37
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops
LE: Logic Element

## Slide 38
Logic Element
The Logic element has:
1 four-input LUT
1 registered output
1 combinational output

## Slide 39
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 40
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example
LUT output
0
0
0
1
1
0
1
1
0
1
0
0
data 2
0
0
0
0
0
0
0
1
1
0
1
1
1
1
1
1
0
0
1
0
X
X
X
X
X
X
X
X
data 1
(
A
)
(
B
)
(
C
)
(
X
)
data 1
0
A
B
0
Y
data 4
data 3
data 2
data 3
data 4
LUT
data 1
0
A
B
C
X
data 2
data 3
data 4
LUT
LUT output
0
1
0
1
0
0
1
0
data 2
0
0
1
1
X
X
X
X
data 1
(
A
)
(
B
)
(Y
)
data 4
data 3
X
X
X
X
LE 1
LE 2

## Slide 41
Using a CAD tool
  Enter the design using schematic entry or an HDL
  Simulate the design
  Synthesize design (create the configuration bitstream)
  Download the configuration onto the FPGA
  Test the design
FPGA Design Flow