## Slide 1
ALU should perform:
Addition
Subtraction
AND
OR
ALU: Arithmetic Logic Unit

## Slide 2
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR

## Slide 3
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR

## Slide 4
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl = 00
Result = A + B

## Slide 5
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B

## Slide 6
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
ALUControl1:0 = 11
Mux selects output of OR gate as Result, so
Result = A OR B

## Slide 7
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B

## Slide 8
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl1:0 = 00
ALUControl0 = 0, so:
Cin to adder = 0
2nd input to adder is B
Mux selects Sum as Result, so
Result = A + B

## Slide 9
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALU with Status Flags

## Slide 10
ALU with Status Flags

## Slide 11
ALU with Status Flags: Negative
N = 1 if:
Result is negative
So, N is connected to most significant bit of Result

## Slide 12
ALU with Status Flags: Zero
Z = 1 if:
all of the bits of Result are 0

## Slide 13
ALU with Status Flags: Carry
C = 1 if:
Cout of Adder is 1
AND
ALU is adding or subtracting (ALUControl is 00 or 01)

## Slide 14
ALU with Status Flags: oVerflow
V = 1 if:
The addition of 2 same-signed numbers produces a result with the opposite sign

## Slide 15
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)

## Slide 16
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs

## Slide 17
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition OR
A and B have different signs upon subtraction

## Slide 18
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition (ALUControl0 = 0) OR
A and B have different signs upon subtraction
(ALUControl0 = 1)

## Slide 19
ALU with Status Flags

## Slide 20
Esercizio PLA

## Slide 21
Esercizio PLA

## Slide 22
Esercizio PLA

## Slide 23
Esercizio PLA

## Slide 24
Esercizio PLA

## Slide 25
Esercizio PLA

## Slide 26
Esercizio PLA

## Slide 27
Esercizio PLA