## Slide 1
<= is nonblocking assignment
  Occurs simultaneously with others
= is blocking assignment
  Occurs in order it appears in file
// Good synchronizer using
// nonblocking assignments
module syncgood(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 <= d; // nonblocking
q <= n1; // nonblocking
end
endmodule
// Bad synchronizer using
// blocking assignments
module syncbad(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 = d; // blocking
q = n1; // blocking
end
endmodule
Blocking vs. Nonblocking Assignment

## Slide 2
Synchronous sequential logic: use always_ff @(posedge clk)and nonblocking assignments (<=)
always_ff @ (posedge clk)
q <= d; // nonblocking
Simple combinational logic: use continuous assignments (assign…)
assign y = a & b;
More complicated sequential logic: use blocking assignments (=) only for intermediate results
More complicated combinational logic: use always_comb and blocking assignments (=)
Assign a signal in only one always statement or continuous assignment statement (if you are not using ‘Z’ values).
Rules for Signal Assignment

## Slide 3
If generic always is used, sensitivity list MUST include all signals used in the always.
Blocking assignments can create latches. Avoid write after read with blocking assignments
all outputs should have default values or must be assigned for every input combination. If not, a latch will be generated to hold the current value.
The actual non-blocking assignment is the last one evaluated
General Rules for Combinational Logic

## Slide 4
Three blocks:
  next state logic
  state register
  output logic
Finite State Machines (FSMs)
Notes: Fine lezione 11

## Slide 5
The double circle indicates the reset state
FSM Example: Divide by 3

## Slide 6
module divideby3FSM (input logic clk,
input logic reset,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype [1:0] state, nextstate;
// state register
always_ff @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: nextstate = S1;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S0);
endmodule
FSM in SystemVerilog

## Slide 7
2:1 mux:
module mux2
#(parameter width = 8) // name and default value
(input logic [width-1:0] d0, d1,
input logic s,
output logic [width-1:0] y);
assign y = s ? d1 : d0;
endmodule
Instance with 8-bit bus width (uses default):
mux2 myMux(d0, d1, s, out);
Instance with 12-bit bus width:
mux2 #(12) lowmux(d0, d1, s, out);
Parameterized Modules

## Slide 8
HDL that tests another module: device under test (dut)
Not synthesizeable
Types:
  Simple
  Self-checking
  Self-checking with testvectors
Testbenches

## Slide 9
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
Name the module sillyfunction
Testbench Example

## Slide 10
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
module sillyfunction(input logic a, b, c,
output logic y);
assign y = ~b & ~c | a & ~b;
endmodule
Testbench Example

## Slide 11
module testbench1();
logic a, b, c;
logic y;
// instantiate device under test
sillyfunction dut(a, b, c, y);
// apply inputs one at a time
initial begin
a = 0; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
a = 1; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
end
endmodule
Simple Testbench

## Slide 12
module testbench2();
logic a, b, c;
logic y;
sillyfunction dut(a, b, c, y); // instantiate dut
initial begin // apply inputs, check results one at a time
a = 0; b = 0; c = 0; #10;
if (y !== 1) $display("000 failed.");
c = 1; #10;
if (y !== 0) $display("001 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("010 failed.");
c = 1; #10;
if (y !== 0) $display("011 failed.");
a = 1; b = 0; c = 0; #10;
if (y !== 1) $display("100 failed.");
c = 1; #10;
if (y !== 1) $display("101 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("110 failed.");
c = 1; #10;
if (y !== 0) $display("111 failed.");
end
endmodule
Self-checking Testbench

## Slide 13
Testvector file: inputs and expected outputs
Testbench:
  Generate clock for assigning inputs, reading outputs
  Read testvectors file into array
  Assign inputs, expected outputs
  Compare outputs with expected outputs and report errors
Testbench with Testvectors

## Slide 14
Testbench clock:
  assign inputs (on rising edge)
  compare outputs with expected outputs (on falling edge).
Testbench clock also used as clock for synchronous sequential circuits
Testbench with Testvectors

## Slide 15
File: example.tv
contains vectors of abc_yexpected
000_1
001_0
010_0
011_0
100_1
101_1
110_0
111_0
Testvectors File

## Slide 16
module testbench3();
logic clk, reset;
logic a, b, c, yexpected;
logic y;
logic [31:0] vectornum, errors; // bookkeeping variables
logic [3:0] testvectors[10000:0]; // array of testvectors
// instantiate device under test
sillyfunction dut(a, b, c, y);
// generate clock
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
1. Generate Clock

## Slide 17
// at start of test, load vectors and pulse reset
initial
begin
$readmemb("example.tv", testvectors);
vectornum = 0; errors = 0;
reset = 1; #27; reset = 0;
end
// Note: $readmemh reads testvector files written in
// hexadecimal
2. Read Testvectors into Array

## Slide 18
// apply test vectors on rising edge of clk
always @(posedge clk)
begin
#1; {a, b, c, yexpected} = testvectors[vectornum];
end
3. Assign Inputs & Expected Outputs

## Slide 19
// check results on falling edge of clk
always @(negedge clk)
if (~reset) begin // skip during reset
if (y !== yexpected) begin
$display("Error: inputs = %b", {a, b, c});
$display(" outputs = %b (%b expected)",y,yexpected);
errors = errors + 1;
end
// Note: to print in hexadecimal, use %h. For example,
// $display(“Error: inputs = %h”, {a, b, c});
4. Compare with Expected Outputs

## Slide 20
// increment array index and read next testvector
vectornum = vectornum + 1;
if (testvectors[vectornum] === 4'bx) begin
$display("%d tests completed with %d errors",
vectornum, errors);
$finish;
end
end
endmodule
// === and !== can compare values that are 1, 0, x, or z.
4. Compare with Expected Outputs

## Slide 21
module adder #(parameter N = 8)
(input logic [N–1:0] a, b,
input logic cin,
output logic [N–1:0] s,
output logic cout);
assign {cout, s} = a + b + cin;
endmodule
ADDER

## Slide 22
module comparator #(parameter N = 8)
(input logic [N–1:0] a, b,
output logic eq, neq, lt, lte, gt, gte);
assign eq = (a == b);
assign neq = (a != b);
assign lt = (a < b);
assign lte = (a <= b);
assign gt = (a > b);
assign gte = (a >= b);
endmodule
COMPARATORS

## Slide 23
module shiftreg #(parameter N = 8)
(input logic clk,
input logic reset, load,
input logic sin,
input logic [N–1:0] d,
output logic [N–1:0] q,
output logic sout);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (load) q <= d;
else q <= {q[N–2:0], sin};
assign sout = q[N–1];
endmodule
SHIFT REGISTER WITH PARALLEL LOAD

## Slide 24
module ram #(parameter N = 6, M = 32)
(input logic clk,
input logic we,
input logic [N–1:0] adr,
input logic [M–1:0] din,
output logic [M–1:0] dout);
logic [M–1:0] mem [2**N–1:0];
always_ff @(posedge clk)
if (we) mem [adr] <= din;
assign dout = mem[adr];
endmodule
RAM

## Slide 25
module rom(input logic [1:0] adr,
output logic [2:0] dout):
always_comb
case(adr)
2'b00: dout = 3'b011;
2'b01: dout = 3'b110;
2'b10: dout = 3'b100;
2'b11: dout = 3'b010;
endcase
endmodule
ROM

## Slide 26
module counter #(parameter N = 8)
(input logic clk,
input logic reset,
output logic [N–1:0] q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else q <= q + 1;
endmodule
COUNTER

## Slide 27
Free tools
Simulatore (icarus verilog):
sudo apt-get iverilog
Sintesi (yosys):
sudo apt-get yosys
Visualizzatore schematici
sudo npm install -g netlistsvg
Visualizzatore waveforms
sudo apt-get gtkwave

## Slide 28
Esempio contatore: simulazione
$ iverilog -o tb counter_tb.v counter.v
$ vvp tb
$ gtkwave test.vcd

## Slide 29
Esempio sommatore: sintesi
$ yosys synth.ys
$ netlistsvg carryadd.js -o carryadd.svg
$ ristretto carryadd.svg

## Slide 30
Esempio contatore: sintesi (RTL)
$ yosys synth_count.ys
$ netlistsvg counter_rtl.js -o counter_rtl.svg
$ ristretto counter_rtl.svg

## Slide 31
Esempio contatore: sintesi (gates)
$ netlistsvg counter.js -o counter.svg
$ ristretto counter.svg