## Slide 1
Exercise 4.5 Write an HDL module called minority. It receives three inputs, a, b, and c. It produces one output, y, that is TRUE if at least two of the inputs are FALSE.
Exercises

## Slide 2
Exercise 4.5 Write an HDL module called minority. It receives three inputs, a, b, and c. It produces one output, y, that is TRUE if at least two of the inputs are FALSE.
module minority(input logic a, b, c, output logic y);
assign y = ~a & ~b | ~a & ~c | ~b & ~c;
endmodule
Exercises

## Slide 3
Exercise 4.6 Write an HDL module for a hexadecimal seven-segment display decoder. The decoder should handle the digits A, B, C, D, E, and F as well as 0–9.
Exercises

## Slide 4
Exercise 4.6 Write an HDL module for a hexadecimal seven-segment display decoder. The decoder should handle the digits A, B, C, D, E, and F as well as 0–9.
Exercises
module sevenseg(input logic [3:0] data,
output logic [6:0] segments);
always_comb
case (data)
// abc_defg
4'h0: segments = 7'b111_1110;
4'h1: segments = 7'b011_0000;
4'h2: segments = 7'b110_1101;
4'h3: segments = 7'b111_1001;
4'h4: segments = 7'b011_0011;
4'h5: segments = 7'b101_1011;
4'h6: segments = 7'b101_1111;
4'h7: segments = 7'b111_0000;
4'h8: segments = 7'b111_1111;
4'h9: segments = 7'b111_0011;
4'ha: segments = 7'b111_0111;
4'hb: segments = 7'b001_1111;
4'hc: segments = 7'b000_1101;
4'hd: segments = 7'b011_1101;
4'he: segments = 7'b100_1111;
4'hf: segments = 7'b100_0111;
endcase
endmodule

## Slide 5
Exercise 4.7 Write a self-checking testbench for Exercise 4.6.
Exercises

## Slide 6
Exercise 4.7 Write a self-checking testbench for Exercise 4.6.
Exercises
module ex4_7_testbench();
logic clk, reset;
logic [3:0] data;
logic [6:0] s;
// instantiate device under test
sevenseg dut(data, s);
initial begin // apply inputs, check results one at a time
data = 4’h0; #10;
if (s !== 7'b111_1110) $display(“0 failed.");
data = 4’h1; #10;
if (s !== 7'b011_0000) $display(“1 failed.");
data = 4’h2; #10;
if (s !== 7'b110_1101) $display(“2 failed.");
…
end
endmodule

## Slide 7
Exercise 4.26 Write an HDL module for an SR latch.
Exercises

## Slide 8
Exercise 4.26 Write an HDL module for an SR latch.
module srlatch(input logic s, r,
output logic q, qbar);
always @(*)
case ({s,r})
2'b01: {q, qbar} = 2'b01;
2'b10: {q, qbar} = 2'b10;
2'b11: {q, qbar} = 2'b00;
endcase
endmodule
Exercises

## Slide 9
Exercise 4.24 Sketch the state transition diagram for the FSM described by the following HDL code.
Exercises

## Slide 10
Exercise 4.24 Sketch the state transition diagram for the FSM described by the following HDL code.
Exercises

## Slide 11
Exercise 4.25 Sketch the state transition diagram for the FSM described by the
following HDL code. An FSM of this nature is used in a branch predictor on some
microprocessors.
Exercises

## Slide 12
Exercise 4.25 Sketch the state transition diagram for the FSM described by the
following HDL code. An FSM of this nature is used in a branch predictor on some
microprocessors.
Exercises

## Slide 13
Exercise 4.48 Consider the following two SystemVerilog modules. Do they have the same function? Sketch the hardware each one implies.
Exercises

## Slide 14
Exercise 4.48 Consider the following two SystemVerilog modules. Do they have the same function? Sketch the hardware each one implies.
Risposta: Si! Hanno la stessa funzione.
Exercises

## Slide 15
Exercise 4.49 Repeat Exercise 4.48 if the <= is replaced by = in every assignment
Exercises

## Slide 16
Exercise 4.49 Repeat Exercise 4.48 if the <= is replaced by = in every assignment
Risposta: No! Non hanno la stessa funzione.
Exercises

## Slide 17
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Exercises

## Slide 18
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Risposta: manca d alla sensitivity list dell’always
Exercises

## Slide 19
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Exercises

## Slide 20
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Risposta: manca b alla sensitivity list dell’always. Le soluzioni sono:
always(a,b)
oppure
always_comb
Exercises

## Slide 21
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Exercises

## Slide 22
Exercise 4.50 The following SystemVerilog modules show errors that the authors have seen students make in the laboratory. Explain the error in each module and show how to fix it.
Risposta:
out1 e out2 non sono assegnati in tutti i casi nell’ always_comb .
Manca il segnale di reset
Exercises