## Slide 1
Exercises
Exercise 5.29 Express the following base 10 numbers in 16-bit fixed-point sign/magnitude format with eight integer bits and eight fraction bits. Express your answer in hexadecimal.
(a) −13.5625
(b) 42.3125
(c) −17.15625
Exercise 5.31 Express the base 10 numbers in Exercise 5.29 in 16-bit fixed-point two’s complement format with eight integer bits and eight fraction bits. Express your answer in hexadecimal.
Exercise 5.33 Express the base 10 numbers in Exercise 5.29 in IEEE 754 single precision
floating-point format. Express your answer in hexadecimal.

## Slide 2
Exercises
Exercise 5.35 Convert the following two’s complement binary fixed-point numbers to base 10. The implied binary point is explicitly shown to aid in your interpretation.
(a) 0101.1000
(b) 1111.1111
(c) 1000.0000
Exercise 5.38 Add the following IEEE 754 single-precision floating-point numbers.
(a) C0123456 + 81C564B7
(b) D0B10301 + D1B43203
(c) 5EF10324 + 5E039020

## Slide 3
Esercizi
Convertire i seguenti numeri in IEEE 754 half-precision e scrivere la codifica esadecimanle corrispondente
−1.5625 × 10−1
(b) 1.771 × 103
(c) 0.34375