## Slide 1
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged
Boolean Algebra

## Slide 2
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 3
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR
Dual: Replace: • with +
0 with 1

## Slide 4
Boolean Axioms
Number | Axiom | Dual | Name
A1 | B = 0 if B ≠ 1 | B = 1 if B ≠ 0 | Binary Field
A2 | 0 = 1 | 1 = 0 | NOT
A3 | 0 • 0 = 0 | 1 + 1 = 1 | AND/OR
A4 | 1 • 1 = 1 | 0 + 0 = 0 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | 1 + 0 = 0 + 1 = 1 | AND/OR
Dual: Replace: • with +
0 with 1
Notes: fine lezione 2

## Slide 5
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements

## Slide 6
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements
Dual: Replace: • with +
0 with 1

## Slide 7
Boolean Theorems of One Variable
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 8
B 1 = B
B + 0 = B
T1: Teorema dell’identità

## Slide 9
B 1 = B
B + 0 = B
T1: Teorema dell’identità

## Slide 10
B 0 = 0
B + 1 = 1
T2: Teorema annullamento

## Slide 11
B 0 = 0
B + 1 = 1
T2: Teorema annullamento

## Slide 12
B B = B
B + B = B
T3: Teorema dell'idempotenza

## Slide 13
B B = B
B + B = B
T3: Teorema dell'idempotenza

## Slide 14
T4: Teorema dell'involuzione (o della doppia negazione)
B = B

## Slide 15
T4: Teorema dell'involuzione (o della doppia negazione)
B = B

## Slide 16
B B = 0
B + B = 1
T5: Teorema dei complementi

## Slide 17
B B = 0
B + B = 1
T5: Teorema dei complementi

## Slide 18
Recap: Basic Boolean Theorems
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identità
T2 | B • 0 = 0 | B + 1 = 1 | Annullamento
T3 | B • B = B | B + B = B | Idempotenza
T4 | B = B |  | Involuzione
T5 | B • B = 0 | B + B = 1 | Complemento
Dual: Replace: • with +
0 with 1

## Slide 19
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 20
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento
How do we prove these are true?

## Slide 21
How to Prove
Method 1: Perfect induction
Method 2: Use other theorems and axioms to simplify the equation
  Make one side of the equation look like the other

## Slide 22
Proof by Perfect Induction
Also called: proof by exhaustion
Check every possible input value
If two expressions produce the same value for every possible input combination, the expressions are equal

## Slide 23
Example: Proof by Perfect Induction
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
0 0
0 1
1 0
1 1
B C BC CB

## Slide 24
0 0
0 0
0 0
1 1
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
Example: Proof by Perfect Induction
0 0
0 1
1 0
1 1
B C BC CB

## Slide 25
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 26
T7: Proprietà associativa
Number | Theorem | Name
T7 | (B•C) • D = B • (C • D) | Proprietà associativa

## Slide 27
T8: Proprietà distributiva
Number | Theorem | Name
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva

## Slide 28
T9: Assorbimento
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 29
T9: Assorbimento
Prove true by:
Method 1: Perfect induction
Method 2: Using other theorems and axioms
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 30
T9: Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
Method 1: Perfect Induction
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 31
T9: Assorbimento
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 32
T9: Assorbimento
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 33
T9: Assorbimento
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento
Method 2: Prove true using other axioms and theorems.

## Slide 34
T9: Assorbimento
Method 2: Prove true using other axioms and theorems.
B•(B+C) = B•B + B•C T8: P. distributiva
= B + B•C T3: Idempotenza
= B•(1 + C) T8: P. distributiva
= B•(1) T2: Annullamento
= B T1: Identità
Number | Theorem | Name
T9 | B• (B+C) = B | Assorbimento

## Slide 35
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento (assorbimento del complemento)
T10: IIo teorema dell’assorbimento
Prove true using other axioms and theorems:

## Slide 36
T10: IIo teorema dell’assorbimento
Prove true using other axioms and theorems:
B•C + B•C = B•(C+C) T8: P. Distributiva
= B•(1) T5’: Complemento
  = B T1: Identità
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento

## Slide 37
Number | Theorem | Name
T6 | B•C = C•B | Proprietà commutativa
T7 | (B•C) • D = B • (C • D) | Proprietà associativa
T8 | B • (C + D) = (B•C) + (B•D) | Proprietà distributiva
T9 | B• (B+C) = B | Io teorema dell’assorbimento
T10 | (B•C) + (B•C) = B | IIo teorema dell’assorbimento
Boolean Theorems of Several Vars
(duality)

## Slide 38
Dual: Replace: • with +
0 with 1
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars

## Slide 39
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars
Warning: T8’ differs from traditional algebra:
OR (+) distributes over AND (•)

## Slide 40
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | P. commutativa
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | P. associativa
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | P. distributiva
T9 | B • (B+C) = B | B + (B•C) = B | Io T. assorbimento
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | IIo T. assorbimento
Boolean Theorems of Several Vars
Axioms and theorems are useful for simplifying equations.

## Slide 41
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals

## Slide 42
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C

## Slide 43
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C
Also called minimizing the equation

## Slide 44
Simplification methods
P. distributiva (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Io T. assorbimento (T9’) A + AP = A
IIo T. assorbimento (T10) PA + PA = P

## Slide 45
Simplification methods
P. distributiva (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Io T. assorbimento (T9’) A + AP = A
IIo T. assorbimento (T10) PA + PA = P
Espansione P = PA + PA
A = A + AP
Duplicazione A = A + A
Esempio di “semplificazione” PA + A = P + A
    PA + A = P + A

## Slide 46
Example
PA + A = P + A
Method 1: PA + A = PA + (A + AP) T9’ Assorbimento
= PA + PA + A T6 P. commutativa
= P(A + A) + A T8 P. distributiva
= P(1) + A T5’ Complemento
= P + A T1 Identità

## Slide 47
PA + A = P + A
Method 2: PA + A = (A + A) (A + P) T8’ P. distributiva
= 1(A + P) T5’ Complemento
= A + P T1 Identità
Example

## Slide 48
Y = AB + AB
Simplifying Boolean Equations
Example 1:

## Slide 49
Y = AB + AB
Y = A T10: II T. assorbimento
or
= A(B + B) T8: P. distributiva
= A(1) T5’: Complemeno
= A T1: Identità
Simplifying Boolean Equations
Example 1:

## Slide 50
Y = A(AB + ABC)
Example 2:
Simplifying Boolean Equations

## Slide 51
Y = A(AB + ABC)
= A(AB(1 + C)) T8: P. distributiva
= A(AB(1)) T2’: Annullamernto
= A(AB) T1: Identità
= (AA)B T7: P. associativa
= AB T3: Idempotenza
Example 2:
Simplifying Boolean Equations